## Slide 1
OPERATING SYSTEMS & KERNEL PROGRAMMING
Process CPU & Memory Inspector
Design and Initial Implementation of a Linux Process Inspector
REVIEW 2 | REQUIREMENT ANALYSIS → DESIGN → FIRST WORKING PARSER
TEAM 6
Hemanth • 2510030326
Yeshwanth • 510030357
Akshith • 2510030365
Parimal • 2510030368
Koneru Lakshmaiah Education Foundation • Department of ECE

## Slide 2
Review 2 — Objectives & Milestone
REVIEW 2
OPERATING SYSTEMS & KERNEL PROGRAMMING | Process CPU & Memory Inspector
REVIEW 2 • 2
Problem identified
Linux exposes useful process information, but raw /proc files require manual inspection and interpretation.
Planned solution
Build a small C utility that accepts a PID, reads selected process fields and prints a compact report.
Review 2 target
Prove the basic file-reading and parsing path first; advanced CPU and system-memory analysis can follow.
Milestone sequence
Understand /proc
→
Design data flow
→
Implement parser
→
Test PID cases
Scope discipline: Review 2 focuses on the first reliable process report, not the final monitoring feature set.

## Slide 3
Why Linux /proc?
REVIEW 2
OPERATING SYSTEMS & KERNEL PROGRAMMING | Process CPU & Memory Inspector
REVIEW 2 • 3
Virtual filesystem
The kernel generates entries dynamically. Process information can be read without parsing a disk-based log.
Per-process directory
A process is represented under /proc/<PID>/; status contains human-readable key/value fields.
User-space access
Standard C file I/O can read the pseudo-file. No custom kernel module is required for this scope.
Example files considered
• /proc/<PID>/status — readable process attributes
• /proc/<PID>/stat — compact scheduler/process data
• /proc/meminfo — system-wide memory counters
• /proc/stat — CPU counters used in a later enhancement

## Slide 4
Requirements & Functional Scope
REVIEW 2
OPERATING SYSTEMS & KERNEL PROGRAMMING | Process CPU & Memory Inspector
REVIEW 2 • 4
Functional requirements
• Receive a process ID (PID)
• Construct the matching /proc path
• Read selected fields
• Display a clear terminal report
Non-functional requirements
• Use bounded buffers
• Handle missing or invalid processes
• Close files after reading
• Keep dependencies minimal
Initial process attributes
Name
→
State
→
PPid
→
VmRSS
These fields form a small but useful first version of the inspector.

## Slide 5
System Design — First Version
REVIEW 2
OPERATING SYSTEMS & KERNEL PROGRAMMING | Process CPU & Memory Inspector
REVIEW 2 • 5
User PID
→
Path builder
→
/proc/<PID>/status
→
Parser
→
Terminal report
Input layer
Read a PID and ensure it is a plausible positive process identifier.
Parsing layer
Read one line at a time and compare known field prefixes.
Output layer
Print only the required fields and release the open file stream.
Design principle: separate path creation, file access, field extraction and reporting.

## Slide 6
Core Logic: Build, Open, Read
REVIEW 2
OPERATING SYSTEMS & KERNEL PROGRAMMING | Process CPU & Memory Inspector
REVIEW 2 • 6
1 Build a bounded path
snprintf(path, sizeof(path), "/proc/%d/status", pid);
The target path is created dynamically from the requested PID. snprintf() limits writes to the destination buffer.
2 Open the pseudo-file
FILE *fp = fopen(path, "r");
if (fp == NULL) { /* report error */ }
Opening can fail when a PID does not exist or access is denied, so the return value must be checked.
3 Stream lines
while (fgets(line, sizeof(line), fp) != NULL) { ... }
Line-by-line reading avoids loading the entire status file into one large buffer.
4 Release resources
fclose(fp);
Close the stream after parsing so resources are not left open.

## Slide 7
Field Extraction — Main Parsing Logic
REVIEW 2
OPERATING SYSTEMS & KERNEL PROGRAMMING | Process CPU & Memory Inspector
REVIEW 2 • 7
Illustrative C snippet
if (strncmp(line, "Name:", 5) == 0 ||
strncmp(line, "State:", 6) == 0 ||
strncmp(line, "PPid:", 5) == 0 ||
strncmp(line, "VmRSS:", 6) == 0) {
printf("%s", line);
}
strncmp()
Compares only the prefix length needed for a field label.
Selected keys
Name, State, PPid and VmRSS are printed; unrelated lines are ignored.
Why this is enough
The first version turns raw kernel text into a compact report.
This snippet illustrates the central parsing idea, not the entire source file.

## Slide 8
Error Handling & Test Plan
REVIEW 2
OPERATING SYSTEMS & KERNEL PROGRAMMING | Process CPU & Memory Inspector
REVIEW 2 • 8
Valid PID
Input: an existing process ID
Expected: selected status fields are printed.
Self inspection
Input: getpid()
Expected: report for the running inspector process.
Missing PID
Input: a non-existent PID
Expected: open failure is reported without a crash.
Verification approach
• Compare field names and values with cat /proc/<PID>/status.
• Cross-check PID, PPID, state and resident memory with ps.
• Treat changing memory values as runtime observations, not fixed expected constants.
Test plan describes intended checks; machine-dependent values must be captured during a live run.

## Slide 9
Build & Demonstration Plan
REVIEW 2
OPERATING SYSTEMS & KERNEL PROGRAMMING | Process CPU & Memory Inspector
REVIEW 2 • 9
Save C source
→
Compile with gcc
→
Run with PID
→
Compare output
Build command
gcc -Wall -Wextra -O2 process_inspector.c -o process_inspector
Example execution
./process_inspector 1
(or run the interactive version if available)
Demonstration checklist: successful compile • valid PID • readable output • missing PID handled safely • comparison against Linux tools.

## Slide 10
Review 2 Outcome & Next Steps
REVIEW 2
OPERATING SYSTEMS & KERNEL PROGRAMMING | Process CPU & Memory Inspector
REVIEW 2 • 10
Expected outcome for this stage
A working first version that reads /proc/<PID>/status, extracts four fields and handles a file-open failure.
Known limitations
Single-process snapshot; CPU utilization is not yet calculated; system-wide RAM is not yet summarized; no continuous sampling.
Proposed work before Review 3
• Add a menu-driven interface and stronger PID/input validation.
• Use /proc/<PID>/stat for CPU-time counters and calculate a usage estimate.
• Read /proc/meminfo to summarize system memory.
The roadmap above is a plausible development progression, inferred from the later final implementation.